## Slide 2: Air Quality Awareness Week Communicating Air Quality Alerts to the Public
April 2016
Michael Geigert
Air Planning and Standards

## Slide 3: Air Quality and Meteorology
Emissions and meteorology are the two most important factors determining the air quality

## Slide 4: Why Include the Air Quality?
You are the messenger to the people!

## Slide 5: Ambient Air Monitoring in Connecticut
Criteria Pollutants
Forecast Pollutants
Lead Monitoring ceases on 6/30/2016

## Slide 6: Extra Slides

## Slide 7: Ozone and Particulate Matter (PM2.5)
With the new ozone 8-hr NAAQS of 70 ppb, expect more alerts this summer;
Ozone monitoring season runs from March- September; daily forecasting usually begins in May;
PM2.5 monitoring runs year-round;
Expect only a few 24-hr PM2.5 exceedance days per year, generally in the winter.
PM2.5 24-hr NAAQS = 35 µg/m3; Annual = 12 µg/m3
CTDEEP issues air quality forecasts everyday of the year.

## Slide 8: The CT DEEP AQI Web Page

## Slide 9: Sign up for AQI updates on Twitter
Air Quality Updates on Twitter
Follow us on Twitter for Connecticut air quality forecasts and alerts. Tweets are generated by EPA's EnviroFlash system and provide the date and air quality forecast for the selected area.
Twitter updates are available for the following towns in Connecticut:
Bridgeport
Danbury
Greenwich
Groton
Hartford
Madison
Middletown
New Haven
Stafford
Stratford
Torrington
Westport

## Slide 10: Extra Slides

## Slide 11: Where is the Ozone?
Tropopause
Bad!
GOOD!

## Slide 12: What is ground-level ozone?
Ozone is a colorless gas formed when nitrogen oxides (NOx) and volatile organic compounds (VOCs) chemically react in the sun.
Ozone is a major component of smog — especially during the summer, when weather conditions are ripe for ground-level ozone to form.
VOC + NOx + sunlight = OZONE

## Slide 13: What do the AQI values mean?

## Slide 14: Ozone: USG Levels
Ozone Orange: The air quality forecast for tomorrow is unhealthy for sensitive groups (code orange).
Key On-Air Message
Air quality is unhealthy for people in sensitive groups.
Supporting Message/ What Action Should People Take?
Sensitive groups, including people with lung disease (such as asthma), active adults and children should take precautions, such as limiting prolonged outdoor exertion.

## Slide 15: Ozone: Unhealthy Levels
Ozone Red: The air quality forecast for tomorrow is unhealthy for Everyone (code red).
Key On-Air Message:
The air quality forecast for tomorrow is unhealthy for everyone.
Supporting Message/ What Action Should People Take?
Everyone needs to limit prolonged outdoor exertion!

## Slide 16: September 17, 2015- 8-hour Ozone AQI

## Slide 17: Peak Ozone AQI- September 17, 2015

## Slide 18: September 18, 2015- 8-hour Ozone AQI

## Slide 19: Peak Ozone AQI- September 18, 2015

## Slide 20: Surface Analysis Animation September 16, 11:00 am- September 19, 2:00 am
Note the nearly stationary high pressure center over the mid-Atlantic region.
This resulted in light winds and stagnant conditions that tended to trap pollutants in the boundary layer.

## Slide 21: Surface Wind Vector Animation September 17-18, 2015

## Slide 22: September 17th NOAA Model
The publicly available NOAA ozone forecast model is of great value to our forecasters!

## Slide 23: September 18th NOAA Model

## Slide 24: Westport CT Modeled Ozone
Chart: NOAA Model 12z Day Before vs. Airnow Observations Sept 17-18, 2015
| 150917 500 | 150917 600 | 150917 700 | 150917 800 | 150917 900 | 150917 1000 | 150917 1100 | 150917 1200 | 150917 1300 | 150917 1400 | 150917 1500 | 150917 1600 | 150917 1700 | 150917 1800 | 150917 1900 | 150917 2000 | 150917 2100 | 150917 2200 | 150917 2300 | 150918 0 | 150918 100 | 150918 200 | 150918 300 | 150918 400 | 150918 500 | 150918 600 | 150918 700 | 150918 800 | 150918 900 | 150918 1000 | 150918 1100 | 150918 1200 | 150918 1300 | 150918 1400 | 150918 1500 | 150918 1600 | 150918 1700 | 150918 1800 | 150918 1900 | 150918 2000 | 150918 2100 | 150918 2200 | 150918 2300 | 150919 0 | 150919 100 | 150919 200 | 150919 300 | 150919 400
Westport NOAA | 35.37 | 39.66 | 36.27 | 27.18 | 19.42 | 18.39 | 20.5 | 23.01 | 25.61 | 30.29 | 40.84 | 52.47 | 61.62 | 69.62 | 77.21 | 81.11 | 76.6 | 68.81 | 66.83 | 74.54 | 73.92 | 67.62 | 61.27 | 56.15 | 48.73 | 45.99 | 39.96 | 30.42 | 25.38 | 26.7 | 29.37 | 29.83 | 30.49 | 36.13 | 47.3 | 58.27 | 71.25 | 82.58 | 91.6 | 96.72 | 96.52 | 92.88 | 86.7 | 75.55 | 62.15 | 57.16 | 55.73 | 52.63
Airnow | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 10 | 23 | 32 | 42 | 58 | 82 | 101 | 103 | 105 | 101 | 95 | 96 | 90 | 72 | 51 | 17 | 10 | 8 | 3 | 3 | 1 | 1 | 1 | 3 | 14 | 39 | 56 | 55 | 66 | 83 | 87 | 92 | 98 | 85 | 74 | 66 | 59 | 57 | 56 | 22 | 13

## Slide 25: Particle Pollution: USG
Key On-Air Message
The air quality forecast for tomorrow is unhealthy for sensitive groups (code orange) for fine particles.
Supporting Message/ What Action Should People Take?
If you are in a sensitive group, including people with heart or lung disease (such as asthma), older adults and children:
You might want to go for a walk instead of a jog.
Try to cut back your strenuous activities or reschedule them when air quality is better.
Take precautions if you experience any unusual coughing or chest discomfort.

## Slide 26
PM2.5 decreases as the atmosphere becomes well-mixed

## Slide 27: PM2.5 Generally Higher in the Winter, unless…
June 10-11, 2015 Smoke Plume from Canadian Wildfires

## Slide 28: Myths and Facts
MYTH | FACT
Asthma is only a concern during the summer and/or when playing sports. | Asthma is a lung disease, and people with asthma are susceptible to air pollution year-round.
Air quality only affects us when we are outside. | That's right for ozone. But when particle levels are high outdoors, they can also be high indoors.
Air pollution is only a concern in the summer. | Particle pollution, unlike ozone, occurs year-round.
There is nothing I can do about air pollution, so I should just ignore it. | People can reduce their exposure to air pollution by simply checking their daily air quality forecast and using it to adjust their strenuous outdoor activities.
Ozone and particle pollution affect the same groups of people. | People with heart or lung disease, older adults, and children are particularly sensitive to the harmful effects of particle pollution. The sensitive groups for ozone include people with lung disease (but not heart disease), and children and adults who are active outdoors.
The health effects of ozone and particle pollution are the same. | While both ozone and particles have been associated with effects on the lungs, particles have also been associated with effects on the heart and cardiovascular system.
Air pollution is a health concern only for people with lung disease (including asthma) and older adults. | Others can be affected by air pollution, including people with heart disease, active adults and children. And when the air quality forecast is code red - everyone can be affected.

## Slide 29: http://airnow.gov/ Web Page

## Slide 30: http://www.enviroflash.info/

## Slide 31: Typical EnviroFlash Message

## Slide 32
Chart: Days > 8-Hr NAAQS (75 ppb) with Polynomial Trend
| 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Days > 8-Hr NAAQS (75 ppb) | 89 | 90 | 91 | 77 | 59 | 103 | 66 | 82 | 102 | 63 | 56 | 42 | 45 | 62 | 42 | 44 | 46 | 29 | 39 | 38 | 36 | 34 | 35 | 44 | 43 | 23 | 39 | 49 | 26 | 20 | 30 | 29 | 43 | 22 | 6 | 24 | 14 | 27 | 18 | 8 | 22
2015 had 22 Ozone Exceedance Days in CT
The air quality continues to improve despite the expected increase in air quality alerts.

## Slide 33: What to Expect for 2016
Previous large El Nino had increased ozone exceedance days

## Slide 34: April 22nd: First Ozone Exceedance!
NOAA 12z Model
NOAA 06z Model
Cornwall
Middletown

## Slide 35: Temperature vs. Ozone
High Temperature = 76° F
8-hour Ozone = 72 ppb
High Temperature = 79° F
8-hour Ozone = 73 ppb

## Slide 36: Cornwall 48-hr Back Trajectories 20z April 22, 2016
1200 Meters
800 Meters
500 Meters

## Slide 37: Persistent Elevated Ozone over the Southeast

## Slide 38: Questions?